## Slide 1: Topic 8: Function pointer and callback function

## Slide 2: Function pointer
Function pointer: A pointer which direct to the address of a function
The declaration of function pointer
  void (*foo)(int);
  int (*foo)(int, int);
  double (*foo)(int *, int *);
The usage
  To have a prototype first  void func (int x)
  Then assign the pointer by  foo = func;

## Slide 3
#include <stdio.h>
void func1(int x)
{
printf ("function 1: %d\n", x );
}
void func2(int x)
{
printf ("function 2: %d\n", x );
}
int main()
{
void (*foo)(int);
foo = func1;
foo (2); /* calling */
foo = func2;
foo (3); /* calling */
return 0;
}

## Slide 4: Callback function
The application of function pointer
Usage:
  When a function receives a command, you can have a common interface to deal with multiple commands
    For example, the communication protocol in kernel
    The packet may be TCP or UDP
    In the IP layer, there many have a common interface, named segment (control, proto)
      where the Proto can be TCP or UDP

## Slide 5
#include <stdio.h>
/* calling function with callback declaration */
void AddNumbers(int x, int (*ySrc)(int)) {
int z = ySrc(x);
printf("result: %d\n", x + z);
}
/* One possible callback. */
int DoubleY(int y) {
return (2*y);
}
/* Another possible callback. */
int MultiY(int y) {
return (y*y);
}
int main(void) {
AddNumbers(30, DoubleY);
AddNumbers(30, MultiY);
}

## Slide 6
#include <stdio.h>
#include <stdlib.h>
void f1 (int input)
{
printf("you entered %d\n", input);
}
void f2 (int input)
{
printf("here you entered %d\n", input);
}
void f3(int input)
{
printf("this time you entered %d\n", input);
}
int main(void)
{
int choice;
void (*func[3])(int) = {f1, f2, f3};
printf("please choice from 0 to 2: ");
scanf("%d", &choice);
func[choice](choice);
}

## Slide 7: W11- on site assignment
Use the concept of function pointer and callback to implement a bubble sort program
  Choose 0 or 1 to sort by increasing or decreasing order
  No static array is allowed !

## Slide 8: W11- on site assignment 2
Implement a HEX and binary to decimal
  User input h2B  the result will be 43
  User input b1011  the result will be 11
  Use the concept of callback function to implement